SHOP SAFETY TEST

Study Guide

| T | F | Horseplay or practical jokes will not be tolerated in the shop. |
| --- | --- | --- |
| T | F | Running in the shop will be tolerated but only if you are careful. |
| T | F | If you find anything wrong with the tools or equipment in the shop report it at once to the instructor. |
| T | F | An eye shield should be worn while drilling, chiseling, or back-sawing overhead. |
| T | F | Never wear loose clothing or long sleeves while operating any machinery with moving parts. |
| T | F | Clean up grease and oil spills immediately. |
| T | F | Oil or clean all machines while they are in motion |
| T | F | Gasoline can be used as a cleaner. |
| T | F | Diesel should be stored in red safety cans. |
| T | F | It is okay to leave oilcans on the benches or tables. |
| T | F | All portable electrical equipment should be grounded through the ground wire. |
| T | F | Always work in your assigned area. |
| T | F | Never leave tools lying on the floor or on projects. Keep them all on your bench in your work place. |
| T | F | Know where the first aid equipment is located. |
| T | F | Always stand behind moving belts, chains, or other moveable parts. |
| T | F | Report all injuries to your instructor for treatment regardless of how small. |
| T | F | Know where all fire extinguishers are and how they are used. |
| T | F | Always store oily and greasy rags in a fireproof container. |
| T | F | If your clothing catches fire, run for water. |
| T | F | Never weld, chip, grind, hammer, or saw near flammables. |
| T | F | Always use your back to lift heavy objects. |
| T | F | Keep the load away from you while lifting. |
| T | F | Keep a steady upward movement while lifting, avoid jerking or sudden movements. |
| T | F | Always carry long or heavy objects by yourself. |
| T | F | The proper wrench should be selected for the job. |
| T | F | The worker should not rely on the jack or chain hoist to hold up a piece of machinery. Rather, the worker should put a block of wood or some other support under it as well. |
| T | F | Machines should be adjusted while they are in gear. |
| T | F | You should remove the carbon monoxide fumes when operating engines inside a closed shop. |
| T | F | When cranking an engine, sufficient space should be provided. Engines should be mounted or braced. |
| T | F | The mouth should be used to siphon gasoline or diesel. |
| T | F | Contact with water from hot radiator should be avoided. |
| T | F | Workers in the shop should closely watch the other students using the grinder |
| T | F | When grinding small objects hold them against the grinding wheel with pliers or tongs. |
| T | F | As a rule, grinding should not be done on the side of a small grinding wheel (1/2 inch width or less). |
| T | F | The operator should stand on one side of the grinder when starting the machine. |
| T | F | Always use rags to hold work that is to be ground. |
| T | F | Keep fingers off the moving grinding wheel. |
| T | F | Never grind aluminum. |
| T | F | The instructor’s permission is not required before using any power tools. |
| T | F | When drilling, when one starts to break through the material they should press down harder on the drill. |
| T | F | Always mark all metal to be drilled with a punch. |
| T | F | Always remove the drill chuck key before starting the machine. |
| T | F | Shavings on the drill press should be brushed off with your hand before drilling a new piece of stock. |
| T | F | Lubricating oil should be used on a cool drill bit when drilling. |
| T | F | The drill should be slowed by hand. |
| T | F | If something falls on the floor while you are drilling, leave the machine on and pick up what fell. |
| T | F | Use the proper speeds for the different bits and materials. |
| T | F | Never use a dull bit. |
| T | F | Always look around while using a power saw. |
| T | F | You should always reach over the saw to secure stock. |
| T | F | Always keep a firm grip on stock. |
| T | F | Cracked or worn saw blades can be resharpened. |
| T | F | When using the table saw you should use the miter gauge and the rip fence together. |
| T | F | The saw should extend ¼” above the material when crosscutting or ripping. |
| T | F | Wear loose clothes and long sleeves while using a circular saw. |
| T | F | Always use a push stick when ripping stock |
| T | F | All adjustments should be checked after turning on the power saw. |
| T | F | It is dangerous for the operator or anyone else to stand inline with the blade while the saw is in operation. |
| T | F | The saw should be stopped before clearing scraps from the tabletop. |
| T | F | Always pile tools and materials on top of the tablesaw. |
| T | F | Stock should be pulled through the saw by the operator. |
| T | F | Round stock can be safely cut on the table saw. |
| T | F | Always use sharp tools to cut cold metal. |
| T | F | Do not use wrenches that are badly chewed or sprung. |
| T | F | Adjustable wrenches should be used with the jaws facing the direction of pull. |
| T | F | Tools with sharp edges can be carried in your pocket. |
| T | F | Cut away from yourself when using sharp hand tools. |
| T | F | Do not use a file without a handle. |
| T | F | Mushroomed ends on chisels, punches, or any hand tools must be ground off. |
| T | F | Your hand should be kept in front of the screwdriver point. |
| T | F | No hammers with loose handles or chipped faces should be permitted in the shop. |
| T | F | Frayed or worn electrical cord use is permitted in the shop. |
| T | F | Never make repairs to electrical units until you know the current is off. |
| T | F | The National Electrical Code sets rules for electricity in California. |
| T | F | Replace blown fuses with ones of higher amperage. |
| T | F | Disconnect an electrical cord by pulling on the cord rather than the plug. |
| T | F | Never operate the electrical switches on equipment with wet hands. |
| T | F | Do not investigate or try to fix broken or down power lines. |
| T | F | Exposed electrical wires are okay if they are uncovered in the electrical box. |
| T | F | It is okay to leave tools and small pieces of material on the shop floor. |
| T | F | Remove nails from boards before putting them into the scrap pile. |
| T | F | You should never use a ladder that has a broken or missing step. |
| T | F | You should not worry about getting scratched from old lumber; especially lumber that has been around livestock. |
| T | F | Inspect lumber for nails before starting to saw. |
| T | F | Never fuel any engine when it is running or it is hot. |
| T | F | Never use safety shields. |
| T | F | Allow for proper ventilation while running an engine in an enclosed area. |
| T | F | Keep loose clothing away from moving PTO shafts. |
| T | F | If you do not have the right tool for the right job just use whatever you can find. |
| T | F | Never point high-pressure air hoses at anyone. |
| T | F | Never grind sharp corners on projects |
| T | F | If it is stuck or does not fit beat on it until it fits. If it breaks it needed to be replaced anyway. |
| T | F | Never use a tool that is too large for the job. |
| T | F | Never move a patient unless it is a matter of life or death. |
| T | F | It is okay to work on batteries without a face shield and protective clothing. |
| T | F | It is okay to charge or work on any battery without the instructor’s permission and supervision. |
| T | F | Obtain permission from the instructor before using the welding equipment. |
| T | F | Always replace the protective cap before moving any cylinders. |
| T | F | If the threads on the cylinder are rusty, wipe them with an oily rag. |
| T | F | Tighten all cylinder, regulators, and torch fittings with a 15-inch adjustable wrench. |
| T | F | Make sure you have ample ventilation when welding. |
| T | F | Keep all flammable materials beneath you when welding. |
| T | F | You may satisfactorily gas weld without goggles. |
| T | F | Always release regulator pressure screw before opening cylinder valve. |
| T | F | Always open the acetylene cylinder valve all the way. |
| T | F | Keep acetylene pressure below 15psi in the hose. |
| T | F | Never light the torch with a match. |
| T | F | Close acetylene valve first if torch backfires. |
| T | F | When you have finished welding, leave cylinder valves open. |
| T | F | A backfire is more serious than a flashback. |
| T | F | Holding the torch tip too close to the molten metal will cause a backfire. |
| T | F | When the flame reaches the hose or regulators, you have a flashback. |
| T | F | Test for leaks in oxyacetylene equipment with a match. |
| T | F | The oxygen hose may be patched with special rubber tape. |
| T | F | Do not stand directly in front of regulators when opening cylinder valve. |
| T | F | The acetylene regulator may be used on an oxygen cylinder. |
| T | F | Oxygen may be used to operate a pneumatic (air) portable grinder. |
| T | F | If you don’t know the answer to a problem ask the instructor. |
| T | F | It is okay to watch the reflection of an electric arc. |
| T | F | Always roll up your shirtsleeves when welding so as to protect your shirt from catching fire. |
| T | F | Do not lay the electrode on your work. |
| T | F | Always turn your cuffs down before welding. |
| T | F | Do not weld or use a torch directly on concrete floors. |
| T | F | Closed containers may be welded on as long as you have ample ventilation. |
| T | F | It is okay to pick up a piece of hot metal with your welding gloves. |
| T | F | It is okay to submerge your welding gloves in water. They are made of leather and are waterproof. |
| T | F | You must turn off the machines when changing amperage settings. |
| T | F | When chipping a weld, you must always wear a shield or goggles. |
| T | F | Oil will not ignite from arc welding sparks. |
| T | F | There should be at least 1/8” between the tool rest and the grinding wheel. |
| T | F | Breathing is the first thing to look for after an accident. |
| T | F | Steel is a good insulator. |
| T | F | Arc welders may be safely operated while standing in water. |
| T | F | The lower the amperage setting is the cooler the arc is. |
| T | F | The oxygen cylinder is not dangerous because it contains low pressure and will not burn. |
| T | F | The acetylene cylinder contains about 2,000 psi when full. |
| T | F | When mixed acetylene and oxygen are not combustible. |
| T | F | Welding galvanized metal will cause you no harm. |
| T | F | You should never stand in front of the metal cut-off saw when operating it. |
| T | F | You should never use the metal cut-off saw if the abrasive cutting wheel is broken or missing pieces. |
| T | F | It is okay to wear gloves while operating the table saw and other similar equipment. |
| T | F | The Piranha Ironworker is not a dangerous piece of equipment. |
| T | F | It is safe to shear very small pieces of metal with the ironworker. |
| T | F | Safety glasses must be worn at all times in the shop. |
| T | F | The ironworker is designed to have two people operating it at the same time. |
| T | F | It is okay to talk to the operator of a machine while he/she is using it. |
| T | F | Closed toe shoes must be worn in the shop. |
| T | F | It is okay to wear shorts while working in the shop. Bare legs are much cooler allowing you to work harder. |
| T | F | The safety information covered by this test completely covers all aspects of shop safety. |
| T | F | If you are in doubt about safety procedures for an operation you should ask your instructor. |