Steps for building a T Bevel

- Cut all metal pieces to length using an ironworker or hacksaw.

2pc – ¼” x 1” x 6” Mild Steel Flat

1pc – 1/8” x 1” x 8” Aluminum Flat

- File all ends until smooth

- Layout all holes to be drilled with a center punch

- Drill the 2 – 1/4” tap holes first using 13/64” twist drill.  Be sure to clamp all metal together using a vice or on the drill press.

- Tap the holes using a ¼ - 20 NC tapper tap– be sure to use WD-40 or cutting oil.

- Bolt all 3 pieces together using (2) ¼” x ¾” NC Bolts

- Drill the hole for a ¼” NC bolt using a 17/64” drill bit to allow the bolt to slide.

- Remove the Aluminum piece and cut a 45 degree angle as shown in the plans.

- File and clean all edges.  Do not put Aluminum on the grinder!!!

- Assemble all parts back together as per the diagram.  Please stamp your initials on the body (MS).

- Turn in project to be graded.

Rubric

Material Cut Properly	(1/8” – 2 pts)					__________/ 20

Threaded Properly / Quality						__________/ 20

Bolts Installed Properly						__________/ 20

Bolt Measurement / Hole Layout (1/8” – 2 pts)			__________/ 20

Quality of Work (Cleanliness)						__________/ 20

TOTAL								__________/ 100